## Slide 1: Hand gesture recognition for educational and patient recovery application
Student: Iancu Paul
Supervisor: S. l. Dr. Ing. Razvan ITU

## Slide 2: Contents
Introduction
Motivation
Solution description
Results
Technologies used

## Slide 3: Introduction
Hand Gesture Recognition is a hot topic in Human Computer Interaction (HCI)
Can be used for multiple purposes (e.g.: sign language recognition, UI interaction, video games, etc.)
It is a more intuitive method of interaction than regular keyboard and mouse methods

## Slide 4: Motivation
Implement a solution that
  Requires minimum hardware
  Robust
  Has real-time capabilities
  Rotation and scale invariant
A prototype that uses our implemented solution
  Application for educational purposes

## Slide 5: Solution description
Steps of the algorithm:
  Histogram equalization
  Hand extraction
  Distance transform
  Palm point
  Palm radius
  Palm mask points
  Wrist points
  Rotation
  Palm mask
  Fingers extraction
  Fingers’ lines
  Fingers’ status

## Slide 6: Histogram equalization
Used for eliminating brightness problems
Convert image from RGB space to HSV space
Extract image of only the value channel
Apply the CLAHE algorithm for performing histogram equalization on the value channel
Convert from HSV space back to the RGB space

## Slide 7: Hand extraction
Extract hand from background
Convert from RGB space to HSV space
Perform HSV filtering
  Keep only the values within a given range for each channel

## Slide 8: Distance transform
Get the distance transform of the contour of the extracted hand

## Slide 9: Palm point location
Use the distance transform to get the location of the palm center (palm point)
The point in the distance transform with the maximum value

## Slide 10: Palm radius
The radius in which the palm region of the hand is expected to be
Get the closest point on the contour of the hand from the palm point

## Slide 11: Palm mask points
Get the points that represent the contour of the palm region of the hand
Get sample points from the palm radius circle
  For each angle in the interval [0; 360] with increment 1 degree, get the respective point on the palm radius center
For each sampled point get the closest point on the hand contour (palm mask point)

## Slide 12: Wrist points
Get the pair of consecutive palm mask points that have the greatest distance between them (wrist points)

## Slide 13: Rotate image
Rotate the image so that the line defined by the two wrist points is horizontal and cut of the portion of the image below the wrist line

## Slide 14: Finger extraction
Get the palm mask (fill the polygon formed by the palm mask points) and apply it to the rotated hand image

## Slide 15: Finger lines
Get the connected components that represent each finger
Get the bounding box of each finger
Get the center and bottom of a finger and take the line as the orientation of the finger

## Slide 16: Finger status
Identify thumb finger, if it exists (checks if a finger’s center makes an angle of 50 degrees or less with the wrist line)
Get palm line (line with maximum length from the palm region)
Divide the palm line in 4 equal regions (one for each finger except the thumb)
Classify each finger based on
which region its bottom
point falls onto

## Slide 17: Results
On 1000 test images gathered from my web camera, an accuracy of 95% classification was achieved
For testing the solution’s real-time capabilities, a sample video was recorded and used for testing
  In the current implementation, a performance of 15 FPS was achieved
  Will implement a multi-threaded version for achieving greater performance
  Other optimization techniques will be applied

## Slide 18: Technologies used
Python 3.7
OpenCV
NumPy
SciPy

## Slide 19: Thank you!